Heat Capacity Behavior and Structure of Alkan-1-ol/Alkylbenzoate Binary Solvents

Ana M. Navarro, Begoña García, Francisco J. Hoyuelos, Indalecio A. Peñacoba, S. Ibeas and José M. Leal*

Universidad de Burgos, Departamento de Química, 09001 Burgos, Spain.

*Corresponding Author: jmleal@ubu.es

ABSTRACT

Heat capacities for the binary mixtures of methanol with (C1-C4) alkylbenzoates and methylbenzoate with (C1-C11) alkan-1-ols have been measured over the whole composition range at 298.15 K under atmospheric pressure. From the experimental measurements, the derived excess molar heat capacities and partial excess molar heat capacities at infinite dilution have been calculated. A Redlich-Kister-type equation was fitted to these data and the fitting parameters and standard deviations have been evaluated. Likewise, the IR spectra for the same systems have been recorded as a function of composition. The sets of experimental data gathered contribute to shed light into the solvent structure and the underlying molecular interactions between the mixture constituents. The conclusions drawn have been established in terms of solute-solvent and solvent-solvent interactions and the ensuing structural effects between the solvent constituents.

Key words:  heat capacity, IR, n-alcohol, alkylbenzoates, solute-solvent interactions.

INTRODUCTION

Studies on thermodynamic and bulk properties of liquid mixtures represent a useful complementary tool to learn the structural features of the pure constituents and the interactions that govern the mixture behavior.1 Isobaric molar heat capacity, Cp, of liquid mixtures is a key quantity in many settings; knowledge of the Cp values as a function of composition may provide valuable structural information.2 Likewise, excess properties help to describe the effects exerted by the molecular orientation, and contribute to shed light into the governing interactions.3 Excess molar heat capacity, , serves to quantify the structural features, to develop theoretical models4 and to design suitable mixed solvents for industrial processes.5

Aromatic esters are known to display specific behavior due to self-aggregation. In particular, benzoic acid esters are categorized as an important class of solvents; the dipolar, hydrophobic behavior and the easily polarizable  electron system accord these solvents a high selective ability, turning them into suitable materials for a variety of applications. The liquid structure of pure alkylbenzoates has rather scarcely been investigated. Their pronounced dipole moment (( 1.94 D) promotes certain molecular ordering in the pure state;6 dipole moment and dipole-dipole interactions increase with the side-chain length. The role played by the size and molecular geometry must also be considered; long side-chains give way to less planar molecules, hinder the interaction with neighbor dipoles and result in less stable dipolar associates.7 Pure alkylbenzoates self-aggregate by H-bonding and remain as stable dimers, the more so the shorter the side-chain.8 Pure alcohols, on the other hand, are extensively self-associated by H-bonding, the association extent decreasing for larger alcohols.9 H-bonding determines the alcohol structure; open chains, cyclic dimers and dimer/trimer mixtures are viable, primary alcohols displaying higher association ability due to the weaker steric hindrance of the OH group.10,11 Other studies, however, disregard the aggregation stoichiometry, assuming equilibrium between O atoms with and without the lone electron-pairs involved. Hence, H-bonding enthalpies become nearly independent of the alcohol size and the small OH free fraction should, in turn, increase slightly for larger alcohols.12,13

To gain further insight into the structures of alkanol/alkylbenzoate systems,10,14,15 and analyze the size and shape effects on the excess properties, new Cp data were measured and the excess molar heat capacities,  have been calculated at 298.15 K for methanol with methylbenzoate (MB), ethylbenzoate (EB), propylbenzoate (PB) and butylbenzoate (BB) and of MB with eleven n-alcohols, from methanol to undecanol. Also, the IR spectra of the corresponding binary mixtures recorded over the whole composition range have contributed to assess the structural effects of the alcohol size (nC) and alcohol self-association ability and the ester side-chain length as well.

EXPERIMENTAL SECTION

Pure solvents, of the highest purity commercially available, were used without further purification, degassed with ultrasound, dried over Fluka 0.3 nm molecular sieves and kept out of the light before use. The purity of the solvents was assessed by a Perkin-Elmer 990 Gas Chromatograph. The binary mixtures, fully miscible over the whole composition range, were prepared by mass ((10-5 g) using a Mettler AT 261 Delta Range balance, always expressing the mixture composition as x, the alcohol mole fraction. The samples were degassed with ultrasound and injected by syringe into suitably stoppered bottles to prevent the liquids from preferential evaporation.

Density measurements. Densities,  ( g cm-3), were measured with the vibrating-tube computer-controlled DSA 5000 Anton Paar digital densitometer (Tables 1S and 2S, Supporting Information), based on the mechanical oscillator measuring principle and equipped with a Peltier element that ensures thermostatization (( 0.01 K). Calibration was performed with deionized doubly distilled water (Milli-Q, Millipore) and n-nonane (Fluka, 99.2 % GC).14

IR spectra. The IR spectra were recorded with a Nicolet 8700 FT-IR spectrophotometer fitted out with a multireflection crystal; it is ideally suited to analyze low concentration samples with high sensitivity and provides advanced velocity for rapid and slow scanning over the 25000-20 cm-1 spectral range. The Analysis of the deconvolution of the ATR-FTIR spectral data in the 3750.93-2649.76 cm-1 range, was handled using Galactic Grams/AI (version 7.01) computer program (Thermo Galactic, Salem, USA). No smoothing was conducted on the spectra to facilitate the determination of the number of overlapping bands. The spectra were truncated in the desired region and the baseline was corrected for sloping.

Heat capacity measurements. Differential scanning calorimetry (DSC) is most used technique for calorimetric measurements. Molar heat capacities were measured at atmospheric pressure with a highly sensitive (± 0.01 Jmol-1K-1) Setaram Micro DSCIII differential scanning calorimeter, based on the Tian-Calvet principle, which determines the change of heat flow from/to the liquid sample upon temperature scanning; the calorimetric signal is proportional to the heat capacity per unit volume. Evaluation of the CP values of the liquid samples requires the density data of the binary mixtures.

Measuring procedure. Cp measurements were carried out in triplicate by the isothermal step method (±0.03 J(mol-1(K-1), which requires only very small (1mL) samples.2,16,17 The instrument consists of two differentially assembled (reference and measuring) vessels lodged in a calorimetric block immersed in a thermostating liquid (undecane) that ensures constant temperature (K);1718-1920 the assembly is placed in an inert atmosphere.18 Calibration was performed according to the Joule effect method, introducing a temperature correction.18,21 Hexane (Fluka, >99.5 %) was the reference material and butan-1-ol (Aldrich, >99.5 %) the calibration liquid. The special vessels used leave out the presence of vapor and no vapor correction was needed.22

The heat-flow (power)/temperature rate from/to the sample was monitored vs time, while programming the sample temperature.21 Heat capacities were obtained in three steps: i) the differential heat flow was measured with the reference and sample vessels filled up with n-hexane; ii) hexane was replaced by the calibration material in the reference vessel, and iii) hexane was replaced by the sample in the measuring vessel.18 The calibration procedure consists of steps i) and ii), with CP reference data taken from literature.23 In each experiment, temperature and differential heat flow rate were recorded vs time. An overall temperature increment was applied at 0.05 K min-1 scan rate. To minimize convection effects outside the thermostatic zone, positive and negative temperature increments were settled. Heat capacities were obtained as:

(1)

where ( stands for the absolute density, M for the molecular weight and A for the peak surface; subscripts S, R and B refer to heat readings of solvent sample, reference (1-butanol) and blank (n-hexane), respectively.18

RESULTS AND DISCUSSION

The CP values measured for the pure constituents concurred well with literature values (Table 1). Figure 1 shows the CP vs x plot for eleven MB-alkanol systems (Table 3S, Supporting Information). The slopes steadily switched from negative (methanol) to positive (undecanol) and only for nC = 5-6 the CP values became (roughly) composition independent; this feature is consistent with the observed variation in excess molar volumes reported earlier.13 The observed CP profile reflects the change in structure inherent to the distinct types of aggregates formed when the alcohol content was raised.24 On the other hand, the four methanol + alkylbenzoate systems (Table 4S, Supporting Information) always displayed positive deviation (Figure 2); the slope of the CP vs x plot rose with increasing ester chain-length. The polynomial eq 2 was used to fit the two sets of Cp vs x data-pairs (Tables 2 and 3),

(2)

Nonideal behavior in mixed solvents bears relation with (a) difference in size and shape between constituents, (b) molecular reorientation after mixing, and (c)  molecular interactions. The extent of the mixture deviation from ideal behavior can best be described by the derived excess property, i.e., the property in excess compared to an ideal solution of same composition. Excess molar heat capacity, , accounts for the liquid ordering upon mixing; its behavior with the mixture composition reflects the change in the solvent structure and provides a measure of the underlying interactions between constituents.27 The  values were evaluated according to:

(3)

where  and  stand for the alcohol and ester contributions, respectively. The  vs x data (Tables 5S and 6S, Supporting Information) displayed maxima at (roughly) x = 0.5 (Figures 3 and 4). The Redlich-Kister-type polynomial eq 4 was fitted to the values (Tables 4 and 5) as a function of the mixture composition:25

(4)

the proper number of Aj fitting coefficients being evaluated by least-squares.26

Values of  have served to assess breaking/formation of H-bonding in polar and nonpolar mixtures.28,29 For alkanol mixtures, positive  values have been ascribed to two competing effects: alcohol self-association and heteroassociation;4,30 the latter contributes negatively to  as the alcohol size is raised, decreasing the maxima.31  Thus, the  profile accounts for the size and self-associating effects on the solvent structure and solvent association ability.24 H-bonded alcohols raise non-randomness and nonideal behavior.32 Moreover, dipole moments of pure esters increased as the side chain-length was raised, enhancing higher ordering and stronger dipole-dipole interactions, an effect accompanied by a fall in density;14 likewise, the planarity of short esters steadily vanishes as the side-chain is raised. Hence, direct interaction between ester dipole moments is not straightforward, since the larger the distance separation, the less efficient the packing, i.e., geometry features must also be taken into account; the balance between dipole-dipole interaction and geometry effects exerts control of the properties of pure alkylbenzoates. The positive  values obtained over the whole composition range (Figures 3 and 4) reveal that breaking of H-bonded structures of pure alcohols upon mixing primarily contributes to .33,34

Thermal relaxation inherent to complex formation between unlike molecules results in positive  values35 and negative molar excess volumes.14 The  curves for MB + 1-alkanol systems displayed maxima for equimolar content (x ( 0.5) and decreased with a rise in the alcohol size, only methanol deviating from this trend (Figure 3). In other words, a shortening of the alcohol size causes breaking of the alcohol structure in the mixture relative to ideal behavior, raising the value.36 The anomalous value obtained for MB + methanol (between octanol and nonanol, Figure 3, inset), reflects the strongly H-bonded structure and pronounced proton donor ability of pure methanol; this striking feature of MB + methanol is supported by the IR data below and is consistent with the anomalous value reported earlier14 for its internal pressure, defined as the work exerted against the cohesive forces by a liquid undergoing an isothermal expansion that entails a change in internal energy.

For methanol + alkylbenzoate mixtures, the maxima increased with a rise in the ester chain-length (Figure 4, inset) (MB<EB<PB<BB), in line with the variation of Cp for pure esters, an effect ascribed to breaking of the ester dipolar ordering; likewise, the ester ability to break the methanol structure in the mixture increases with the ester chain-length.36 A boost in ordering upon mixing results in positive contribution to , and negative to net order destruction.37 Dispersive interactions, dipole/dipole and dipole/induced dipole attractions contribute to increased  values,38,39 conveying the mixture propensity to non-randomness.40,41 Pure alkanols form strong linear and cyclic O-H-O H-bonds.42 When alcohols mix up with alkylbenzoates, unlike H-bonding associations arise, linking the alcohol OH group with the CO ester group; despite the opposed heteroassociating effect, breaking of self-associated alcohols prevails, since the larger the alcohol chain, the easier the self-aggregation disruption.8

Partial molar functions, which account for the rate of change with concentration of extensive thermodynamic properties due to addition to mixture of an infinitely small amount of one component, provide valuable information on binary and higher order interactions. From the fitting coefficients of excess molar heat capacities (Tables 4 and 5), the partial excess molar property, , was evaluated for the binary constituents according to the intercept method.15 The limiting value at infinite dilution for each constitunt, ,  obtained as the values at mole fraction approaching zero, give a measure of the solute-solvent forces and involve geometry effects and intermolecular interactions. In addition to the intrinsic solute volume, solute-solvent forces are the main factor that governs the solvent packing around a central solute unit. Therefore, an analysis of the values lends a valuable insight into the solvent structure. Table 6 lists the  values for both constituents of the two sets investigated, showing the effect of the number of CH2 groups. For methanol + alkylbenzoates, the  and contributions increased with the rise in the number of CH2 groups of the alkyl chain. By and large, these values decreased for MB + alkanol systems when the alcohol size was raised, reflecting the propensity of polar molecules to clustering.27

The variation of the IR spectra for alkanol + MB and methanol + alkylbenzoate systems with increasing alcohol content, recorded over the whole composition range, are informative of homo and heteroassociations. As an example, Figure 5 shows the variation of the IR spectra upon increase of the alcohol content for methanol + MB. In the 3650-3150 cm-1 range, Figure 5 shows that for methanol + MB system at different mole fractions different bands are obtained from the deconvolution, passing from a very low intensity band for pure MB (Figure 5a) to four bands at intermediate mole fractions (Figures 5b and 5c), and to only a single, high-intensity band for pure alcohol (Figure 5d). Regarding the stretching vibration (O-H, the IR spectra recorded in the above range43 reflect the pronounced effect of H-bonding in alcohols and is informative of alcohol association. The shift of the frequency range also reflects the bond strength and the masses involved.

Depending on the alcohol content, several subsequent bands were obtained from the deconvolution performed (Figures 5b and 5c). The acute band within 3650-3590 cm-1 is ascribed to the free OH. The band within 3600-3450 cm-1 corresponds to OH intramolecularly associated, whose relative intensity does not depend on the alcohol content. The wide band within 3650-3150 cm-1 (whose relative intensity depends on the alcohol content), denoted as (I), corresponds to the intermolecularly associated OH and involves dimer and polymer species.43

Figure 6a shows that the shift of the wavenumber of the peak center of band (I) for alkanol + MB depends on the alcohol size only for high ester content. Figure 7a shows that the shift of the wavenumber of the peak center of band (I) for methanol + alkylbenzoate depends on the ester side-chain length only for high ester content. Figure 6b plots the variation of the Area band (I) with the alcohol content, for alkanol + MB systems, clearly disclosing the much greater Area for methanol compared to pentanol and of pentanol compared to undecanol. Therefore, given that the Area of this band is proportional to the concentration of intermolecular aggregates present, it follows that mixtures with methanol are much more associated. The alcohol structure is not fully distorted after mixing; though somewhat modest relative to the pure constituent, certain alcohol association degree in the mixture still remains. Finally, Figure 7b plots the variation of the Area, band (I), with alcohol content, showing that the heteroassociation effect in methanol + alkylbenzoate systems, strongly depends on the alcohol content and only very little on the ester size and ester content. All these results concur well with the conclusions stemming from the heat capacity measurements discussed above.

CONCLUSIONS

New molar heat capacity data have been measured for alkanol/alkylbenzoate mixtures. The CP values of the pure constituents showed a regular trend, increasing with the number of carbon atoms. The  values for the binary mixtures displayed maxima for equimolar content and deviation from ideality is explained in terms of molecular effects, stressing the H-bonding and dipole moment effects. Breaking of self-associated alkanols is accompanied by nonspecific interactions, namely mixing and packing effects. Three factors govern the alkan-1-ol/alkylbenzoate structures: (i) disruption of alkanol H-bonds; (ii) formation of alkanol-ester aggregates; (iii) the shape and size factors of the components. The aggregates became weakened with an increase in the ester side-chain length and the alcohol size. The conclusions drawn are supported by the variation with the solvent composition of the IR spectra recorded.

ASSOCIATED CONTENT

Supporting Information.- Supporting information for this article, Tables 1S to 6S, is available This material is available free of charge via the Internet at http://pubs.acs.org.

AUTHOR INFORMATION

Corresponding Author

*Tel.: +34 947 258819,  fax: + 34 947 258831.  Email:  jmleal@ubu.es

ACKNOWLEDGMENT

The financial support by Junta de Castilla y León, Project GR257, Ministerio de Educación y Ciencia, Project CTQ2009-13051/BQU, supported by FEDER, and Universidad de Burgos with funding by Caja de Burgos, Spain is gratefully acknowledged.

REFERENCES

(1) Comelli, F.; Bigi, A.; Vitalini, D.; Rubine, K. J. Chem. Eng. Data 2010, 55, 205-210.

(2) Zorębski, E.; Góralski, P.; Tkaczyk, M. J. Chem. Thermodyn. 2005, 37, 281-287.

(3) Checoni, R. F.; Francesconi, A. Z. J. Solution Chem. 2007, 36, 913-922.

(4) Piñeiro, A. Fluid Phase Equilibr. 2004, 216, 245-256

(5) Hanks, R. W.; Christensen, J. J. I. Chem. Symp. Ser. 1979, 56, 29-49.

(6) Riddick, J. A.; Bunger, W. B.; Sakano, T. K. Organic Solvents. Physical Properties and Methods of Purification; 4ª Ed, Ed Wiley: New York, 1986.

(7) Ortega, J.; Postigo, M. Fluid Phase Equilibr. 1995, 108, 121-133.

(8) Hu, J.; Tamura, K.; Murakami, S. Fluid Phase Equilibr. 1997, 131, 197-212.

(9) Navarro, A. M.; García, B.; Peñacoba, I. A.; Hoyuelos, F. J.; Leal, J. M. J. Phys. Chem. B  2011, 115, 10259-10269.

(10) Cerdeiriña, C. A.; Gonzalez-Salgado, D.; Romani, L.; Delgado, M. C.; Torres, L. A.; Costas, M. A. J. Chem. Phys. 2004, 120, 6648-6659.

(11) Huyskens, P. J. Mol. Struct. 1983, 100, 403-414.

(12) Souto-Caride, M.; Troncoso, J.; Losada-Pérez, P.; Peleteiro, J.; Carballo, E.; Romani, L. Chem. Phys. 2009, 358, 225-229

(13) Rubini, K.; Francesconi, R.; Bigi, A.; Comelli, F. Thermochim. Acta, 2007, 452, 124-127.

(14) García, B.; Aparicio, S.; Navarro, A. M.; Alcalde, R.; Leal, J. M. J. Phys. Chem. B 2004, 108, 15841-15850.

(15) García, B.; Alcalde, R.; Aparicio, S.; Leal, J. M. J. Phys. Chem. B 2005, 109, 19908-19914.

(16) Rudtsch, S. Thermochim. Acta 2002, 382, 17-25.

(17) Góralski, P.; Tkaczyk, M.; Chorżewski, M. J. Chem. Eng. Data 2003, 48, 492-496.

(18) Cerdeiriña, C. A.; Míguez, J. A.; Carballo, E.; Tovar, C. A.; de la Puente, E.; Romaní, L. Thermochim. Acta 2000, 347, 37-44.

(19) Cobos, J. C.; García, I.; Casanova, C.; Roux, A. H.; Roux-Desgranges, G.; Grolier, J.-P. E. Fluid Phase Equilibr. 1991, 69, 223-233.

(20) Pérez-Sánchez, G.; Losada-Pérez, P.; Cerdeiriña C. A.; Thoen, J. J. Chem. Phys. 2010, 132, 214503-1-7.

(21) Höhne, G. W. H; Hemminger, W.; Flammersheim H.-J. Differential Scanning Calorimetry, Springer-Verlag: Berlin Heidelberg, 1996.

(22) Lei, Y.; Chen, Z.; Wang, N.; Mao, C.; An, X.; Shen, W. J. Chem. Thermodyn. 2010, 42, 864-872.

(23) a) Zábranský, M.; Ruzicka, V. Jr.; Majer, V.; Domalski, E. S. J. Phys. Chem. Ref. Data 1996, Monograph 6, Vol. I y Vol II; b) Zábranský, M.; Ruzicka, V. Jr.; Domalski, E. S. J. Phys. Chem. Ref. Data 2001, 30, 1199-1691. c) Zábranský, M.; Kolska, Z.; Ruzicka, V.; Domalski, E. S. J. Phys. Chem. Ref. Data 2010, 39, 013103 1-404.

(24) Dzida, M.; Góralski, P. J. Chem Thermodyn. 2009, 41, 402-413.

(25) Redlich, O.; Kister, A. T. Ind. Eng. Chem. 1948, 40, 341-345.

(26) Bevington, P. Data Reduction and Error Analysis for the Physical Sciences. McGraw-Hill: New York, 1969.

(27) Cerdeiriña, C. A.; Tovar, C. A.; González, D.; Carballo, E.; Romaní, L. Fluid Phase Equilibr. 2001, 179, 101-115.

(28) Gepert, M.; Zorebski, E.; Leszcynska, A. Fluid Phase Equilibr. 2005, 233, 157-169.

(29) Patterson, D. Thermochim. Acta, 1995, 267, 15-27.

(30) Calvo, E.; Brocos, P.; Piñeiro, A.; Pintos, M.; Amigo, A.; Bravo, R.; Roux, A. H.; Roux-Desgranges, G.; J. Chem. Eng. Data 1999, 44, 948-954.

(31) Waliszewski, D. J. Chem. Thermodyn. 2008, 40, 203-207.

(32) Souto-Caride, M.; Troncoso, J.; Losada-Pérez, P.; Peleteiro, J.; Carballo, E.; Romani, L.; Chem. Phys. 2009, 360, 106-109.

(33) Schulman, E. M.; Dwyer, D. W.; Doetschman, D. C. J. Phys. Chem. 1990, 94, 7308-7312.

(34) Wallen, S. L.; Palmer, B. J.; Garrett, B. C.; Yonker, C. R. J. Phys. Chem. 1996, 100, 3959-3694.

(35) Tanaka, R. ; Nakamichi, T. J. Chem. Thermodyn. 1997, 29, 221-227.

(36) Peleteiro, J.; Troncoso, J.; Gónzalez-Salgado, D.; Valencia, J. L.; Souto-Caride, M.; Romaní, L. J. Chem. Thermodyn. 2005, 37, 935-940. b) Peleteiro, J. Troncoso, J.; Gónzalez-Salgado, D.; Valencia, J. L.; Cerdeiriña. C. A.; Romaní, L. Int. J. Thermophys. 2004, 25, 787-803.

(37) Calvo-Iglesias, E.; Bravo, R.; Pintos, M.; Amigo, A.; Roux, A. H.; Roux-Desgranges, G. J. Chem. Thermodyn. 2007, 39, 561-567.

(38) Chorażewski, M. J. Chem. Eng. Data 2007, 52, 154-163.

(39) Baluja, S.; Matsuo, T.; Tamura, K. J. Chem. Thermodyn. 2001, 33, 1545-1553.

(40) Pardo, J. M.; Tovar, C. A.; Troncoso, J.; Carballo, E.; Romaní, L. Thermochim. Acta 2005, 433, 128-133.

(41) Peleteiro, J.; González-Salgado D.; Cerdeiriña. C. A.; Romaní, L. J. Chem. Thermodyn. 2002, 34, 485-497.

(42) Jeffrey, G. A. An Introduction to Hydrogen Bonding, Oxford University Press: New York, 1997.

(43) Pretsch, E.; Clero, T; Seibl J.; Simon, W. Tablas para la determinación estructural por métodos espectroscópicos, 3ª Ed, Ed Springer: Barcelona, 2000.

(44) Lide, R. D.; CRC. Handbook of Chemistry and Physics, 83ª Ed., Electronic edition, CRC Press LLC, 2003 http://Hbcpnetbase.com/.

(45) CDATA, Database of Thermodynamic and Transport Properties for Chemistry and Engineering, Version 1.020, Departament of Physical Chemistry, Institute of Chemical Technology, Prague, Czech Republic, 1999.

(46) Comelli, F.; Francesconi, R.; Bigi, A.; Rubini, K. J. Chem. Eng. Data 2006, 51, 1711-1716.

(47) Dzida, M.; Góralski, P. J. Chem. Thermodyn. 2006, 38, 962-969.

(48) van Miltenburg, J. C.; Gabrielová, H.; Růžička, K. J. Chem. Eng. Data 2003, 48, 1323-1331.

TABLES

Table 1. Comparison of the Isobaric Molar Heat Capacity of the Pure Solvents, CP (J(K-1(mol-1) at 298.15 K obtained in this Work with those reported in the Literature.

Table 2. Parameters Aj, Standard Deviation and (2 Coefficients of the Polynomial Equation for Molar Heat Capacitiy, CP, of the {(x) 1-Alkanol+ (1-x) Methylbenzoate} Systems at 298.15 K.

Table 3. Parameters Aj, Standard Deviation and (2 Coefficients of the Polynomial Equation for Molar Heat Capacity, CP, of the {(x) Methanol+ (1-x) Alkylbenzoate} Systems at 298.15 K.

Table 4. Parameters, Aj, Standard Deviation and (2 Coefficients of the Redlich-Kister Equation for Excess Molar Heat Capacity, , of the {(x) 1-Alkanol+ (1-x) Methylbenzoate} Systems at 298.15 K.

Table 5. Parameters, Aj, Standard Deviation and (2 Coefficients, of the Redlich-Kister Equation for the Molar Excess Heat Capacity, , of the {(x) Methanol+ (1-x) Alkylbenzoate} Systems at 298.15 K.

Table 6. Partial Molar Excess Heat Capacity at Infinite Dilution , (a) {(x) 1-Alkanol + (1-x) Methylbenzoate}, (b) {(x) Methanol + (1-x) Alkylbenzoate} Binary Solvents at 298.15 K.

Table 1

| Alkylbenzoate | 1-Alkanol |
| --- | --- |
| MB | EB | PB | BB | C1 | C2 | C3 | C4 | C5 | C6 | C7 | C8 | C9 | C10 | C11 |
| 218.32a 221.3b 221.299c | 247.13a 246d 245.965c | 274.04a 273.42293.15Kb | 304.15a 304.06c | 81.48a 81.47b 81.11c 81.109f 81.3h | 111.92a 112.34b 112.30c 112.29f 112.03k | 144.98a 143.87b 143.90c 143.85f 144.9h 144.61m | 177.10a 177.08b 177.10c 176.48e 176.82l | 208.97a 208.98b 208.10c 208.1d 208.27e | 241.51a 241.32b 240.40c,e 240.4d 240.77j | 273.91a 272.10c 272.1d 272.53e | 306.69a 305.55b 303.90c 305.2d 305.25e | 339.64a 337.57c 337.98e | 373.33a 370.5c 370.6d 371.18e 372.61i 374.6j | 406.65a 406.52c 406.52f |

aThis work, bref 6, cref.23, dref 44, eref 30, fref 45, gref 31¸ href 46, iref 47, jref 48 kref 36, lref 2, mref 41.

Table 2

|  | A0 | A1 | A2 | A3 | A4 | A5 | ( | (2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Methanol | 218.06 | -95.81 | -49.04 | 8.52 | --- | --- | 0.19 | 4.499E-01 |
| Ethanol | 218.27 | -62.51 | -38.21 | -5.17 | --- | --- | 0.29 | 7.422E-01 |
| 1-Propanol | 218.30 | -42.03 | 45.18 | -208.82 | 207.47 | -75.18 | 0.11 | 9.500E-02 |
| 1-Butanol | 218.30 | -9.10 | 32.10 | -176.70 | 181.60 | -69.10 | 0.10 | 2.000E-01 |
| 1-Pentanol | 218.31 | 14.30 | 71.74 | -252.58 | 241.54 | -84.41 | 0.10 | 7.900E-02 |
| 1-Hexanol | 218.29 | 52.87 | 25.97 | -143.99 | 133.59 | -45.27 | 0.10 | 7.700E-02 |
| 1-Heptanol | 218.24 | 86.61 | -4.45 | -45.59 | 19.11 | --- | 0.11 | 1.154E-01 |
| 1-Octanol | 218.17 | 119.06 | -4.28 | -51.84 | 25.72 | --- | 0.19 | 3.157E-01 |
| 1-Nonanol | 218.15 | 153.54 | -19.47 | -29.20 | 16.75 | --- | 0.23 | 4.682E-01 |
| 1-Decanol | 218.10 | 186.60 | -31.70 | --- | --- | --- | 0.30 | 9.000E-01 |
| 1-Undecanol | 218.02 | 217.89 | -32.67 | 3.19 | --- | --- | 0.24 | 5.764E-01 |

Table 3

|  | A0 | A1 | A2 | A3 | A4 | ( | (2 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Ethylbenzoate | 247.09 | -123.79 | -49.43 | 7.84 | --- | 0.19 | 3.764E-01 |
| Propylbenzoate | 274.15 | -148.78 | -52.58 | 9.04 | --- | 0.17 | 3.176E-01 |
| Butylbenzoate | 304.30 | -172.60 | -79.90 | 50.70 | -20.80 | 0.20 | 5.000E-01 |

Table 4

|  | A0 | A1 | A2 | ( | (2 |
| --- | --- | --- | --- | --- | --- |
| Methanol | 36.40 | -2.29 | -1.09 | 0.22 | 6.379E-01 |
| Ethanol | 46.03 | 4.39 | 5.78 | 0.27 | 7.516E-01 |
| Propan-1-ol | 45.74 | 3.50 | -4.38 | 0.16 | 2.801E-01 |
| Butan-1-ol | 44.48 | 4.68 | -2.32 | 0.17 | 3.126E-01 |
| Pentan-1-ol | 42.47 | 4.35 | -7.16 | 0.17 | 3.079E-01 |
| Hexan-1-ol | 40.91 | 2.63 | -4.91 | 0.11 | 1.446E-01 |
| Heptan-1-ol | 39.27 | 4.02 | -5.00 | 0.11 | 1.229E-01 |
| Octan-1-ol | 36.99 | 1.24 | -6.15 | 0.18 | 3.708E-01 |
| Nonan-1-ol | 33.86 | -1.11 | -4.14 | 0.22 | 5.239E-01 |
| Decan-1-ol | 31.40 | -0.86 | -9.11 | 0.16 | 2.744E-01 |
| Undecan-1-ol | 27.83 | -0.86 | -7.90 | 0.09 | 9.520E-02 |

Table 5

|  | A0 | A1 | A2 | ( | (2 |
| --- | --- | --- | --- | --- | --- |
| Ethylbenzoate | 37.85 | -2.93 | 1.98 | 0.19 | 4.294E-01 |
| Propylbenzoate | 39.39 | -3.78 | 5.10 | 0.15 | 2.783E-01 |
| Butylbenzoate | 40.97 | -4.16 | 7.71 | 0.23 | 5.762E-01 |

Table 6

| (a) | Methylbenzoate |  | (b) | Methanol |
| --- | --- | --- | --- | --- |
| Methanol | 28.46 | 41.53 |  | Ethylbenzoate | 35.45 | 43.45 |
| Ethanol | 33.06 | 66.17 |  | Propylbenzoate | 43.82 | 44.76 |
| Propan-1-ol | 31.23 | 49.89 |  | Butylbenzoate | 49.89 | 47.12 |
| Butan-1-ol | 31.74 | 51.29 |  |  |  |  |
| Pentan-1-ol | 23.69 | 45.25 |  |  |  |  |
| Hexan-1-ol | 33.37 | 38.62 |  |  |  |  |
| Heptan-1-ol | 20.34 | 38.28 |  |  |  |  |
| Octan-1-ol | 21.46 | 38.13 |  |  |  |  |
| Nonan-1-ol | 20.58 | 36.51 |  |  |  |  |
| Decan-1-ol | 17.83 | 25.52 |  |  |  |  |
| Undecan-1-ol | 17.21 | 21.92 |  |  |  |  |

CAPTION TO FIGURES

Figure 1. Molar Heat Capacities, CP (J(K-1(mol-1), for (x) Alkan-1-ol + (1-x) (MB) Binary Solvents at 298.15 K. (( Methanol, ( Ethanol, ( Propan-1-ol, ( Butan-1-ol, ( Pentan-1-ol, ( Hexan-1-ol, ( Heptan-1-ol, ( Octan-1-ol, ( Nonan-1-ol, ( Decan-1-ol, ( Undecan-1-ol).

Figure 2. Molar Heat Capacities, CP (J(K-1(mol-1), for (x) Methanol + (1-x) Alkylbenzoate Binary Solvents at 298.15 K. (( Methylbenzoate, ( Ethylbenzoate, ( Propylbenzoate, ( Butylbenzoate).

Figure 3. Molar Excess Heat Capacities,  (J(K-1(mol-1), for (x) Alkan-1-ol + (1-x) (MB) Binary Solvents at 298.15 K. (( Methanol, ( Ethanol, ( Propan-1-ol, ( Butan-1-ol, ( Pentan-1-ol, ( Hexan-1-ol, ( Heptan-1-ol, ( Octan-1-ol, ( Nonan-1-ol, ( Decan-1-ol, ( Undecan-1-ol). Inset: plot of  vs alcohol size, nC, for Equimolar Mixtures (x) Alkan-1-ol + (1-x) (MB) at 298.15 K.

Figure 4. Molar Excess Heat Capacities  (J(K-1(mol-1), for (x) Methanol + (1-x) Alkylbenzoate Binary Solvents at 298.15 K. (( Methylbenzoate, ( Ethylbenzoate, ( Propylbenzoate, ( Butylbenzoate). Insert: plot of  vs alkylbenzoate chain-length nC for Equimolar Mixtures (x) Methanol+ (1-x) Alkylbenzoate at 298.15K.

Figure 5. Deconvolution of ATR-FTIR spectra in the 3750.93-2649.76 cm-1 range for methanol + MB  at 298.15K using Gaussian−Lorentzian functions by the  GRAMS/AI program (version 7.01), (a) pure MB,  (b) methanol + MB  (x = 0.3309), (c) methanol + MB (x =  0.7113), (d) pure methanol. Band (I) in the 3400-3300 cm-1 showing the intermolecular association.

Figure 6:  (a) Variation of the wavenumbers (cm-1) of the peak center  showing the position of the IR band (I), 3650-3200, 3150 cm-1,  (b) variation of the Area  of the IR band (I), 3650-3200, 3150 3400-300 cm-1 for 1-Alkanol + MB  systems at 298.15 K. (( Methanol, ( Pentan-1-ol, ( Undecan-1-ol)

Figure 7:    (a) Variation of the wavenumbers (cm-1) of the peak center  showing the position of the IR band (I), 3650-3200 3150cm-1,  (b) variation of the Area  of the IR band (I),  3650-3200 3150 3400-3300 cm-1 for  methanol +  alkylbenzoate systems at 298.15 K. (( Methylbenzoate, ( Ethylbenzoate, ( Propylbenzoate, ( Butylbenzoate).

Figure 1						Figure 2

Figure 3						Figure 4

Figure 5

Figure 6

Figure 7

TOC GRAPHIC

# Text boxes

(a)

(d)

(I)

(b)

(I)

(c)

(I)

(b)

(a)

(a)

(b)